## Slide 1
HOW DO WE HELP DOTS SAY YES TO CLIMATE-SMART INFRASTRUCTURE?
Bringing ROW Solar to Life
Inesha Gupta, Regional Research Intern
The Ray Highway
8th August, 2025
Exit 14, Georgia | Carbon Reduction Challenge 2025

## Slide 2
DOT’S NEED TOOLS TO QUANTIFY ROW VALUE
  40M acres of DOT-managed ROW land
  Underused space == a Climate Asset
(Webber Energy Group, 2020)
  DOTs aren’t solar developers
  No tools to quantify value
The Challenge
The Opportunity
  Zero carbon, zero waste highways
  Use public land as a climate asset
The Ray’s Role
My Role
Built a model to show:
✔️ Carbon savings
✔️ Cost savings
2

## Slide 3
THE GA EXIT 14 PROJECT SAVES 783 MT CO2 FROM 4 ACRES
3
Project details: 1 MW solar on 4 acres, 26.9% capacity factor, Grid Intensity: 733 lb CO₂/MWh
Assumption: Mowing cost: $2,000/acre → reduced by 40% with pollinator habitat
Carbon Reductions:
Annual CO₂ Saved: 783 metric tons = approx. 1,700 cars off the road
10-Year Impact: 7,833 tCO₂ avoided
Method:
Energy Generated = 1 MW × 8,760 h × 26.9% = 2,356 MWh/year
CO₂ = 2,356 × 733 ÷ 2,204.62

## Slide 4
EVEN WITHOUT OWING, THE DOT COMES OUT AHEAD
4
Cost Savings
Scenario A: DOT-Owned
  Net annual benefit: electricity revenue + cost savings − pollinator mowing cost: $259k
  NPV (10-year, discounted, highest possible value): $1.79M
  Assumptions: GA electricity price, 7.29% discount, $2k/acre mowing reduced by 40%
Scenario B: Lease Model (No CAPEX):
  Annual Revenue: $14,933 (land lease) + $3,200 (mowing savings): $18,133/yr
  NPV (10-year, discounted): $125,000

## Slide 5
CO-BENEFITS AND ROADBLOCKS
5
Co-Benefits:
Biodiversity: Supports pollinators, improves soil & slope stability
Public Perception: Signage and aesthetics improve community trust
Grid Readiness: Prepares ROW for co-use like EV charging hubs
Roadblocks:
  DOT contracting procurement strategies not conducive to realizing mowing cost benefits
  Limited internal DOT capacity to evaluate site feasibility

## Slide 6
NEXT STEPS
6
Next Steps
Current Status:
  Model being tested on Georgia’s Exit 14 site
  Meeting scheduled with GDOT landscape team (Aug 7) to understand replicability and advance model capabilities
Recommendations:
  Use model to communicate ROI to internal stakeholders
  Leverage The Ray’s technical assistance for procurement & grid planning
  Customize for other states using local electricity price, solar potential, and lease rates

## Slide 7
With just 4 acres, DOTs can save 7,833 tCO₂ and generate up to $1.79M in value over 10 years.
THANK YOU!
SOURCE: INESHA GUPTA, CARBON REDUCTION CHALLENGE FINAL REPORT